## Slide 1
IDEA :- Growth pattern to be studied & size to be finalize.
TPM CIRCLE NO :- 01
TPM CIRCLE NAME: Achiever
DEPT :- MACHINE SHOP
CELL:- PRV
CELL NAME:- A225 PRV
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- CNC M/C
OPERATION :- Turning & Gas Nitro carburizing
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A
C
D
S
M
KAIZEN THEME : To eliminate A225 PRV OD o/s
after Nitro carburizing spec.11.45-0.03 actual 11.43 .
Problem present status :-A225 PRV OD oversize spec 11.4-0.03 mm actual observed 11.43 mm .
COUNTERMEASURE:-
1. Semi finished dimension to be change from
Ø11.4 +0.010 to Ø11.4 -0.010
2. Semi finished drawing to be confirm.
3. Ring gauge to be prepared Ø11.4 -0.010
BENCHMARK
TARGET
KAIZEN START
TDC
250 no’s
0 no
25.03.2016
12.05.2016
TEAM MEMBERS :Ganesh Gaikwad,
Sachin Yeole, Santosh Wakchaure ,Ashish ,
Sachin Kadnar
BENEFITS :-
1) In-house rework & rejection will be eliminate.
MANAGER’S SIGN :- Sunil Kinkar
REGISTERED BY :- Ashish Jagtap
REGISTRATION NO. & DATE : 25.03.2016
WHY - WHY ANALYSIS :-
Why1 :- A225 PRV od o/s.
Why2 :- After gas nitro carburizing part get oversize . ( growth observed upto 0.050 mm)
Why3 :-No size calculated for machining before Nitro carburizing
RESULT :-
SCOPE & PLAN FOR HORIZONTAL DEPLOYMENT
SR.
NO.
CELL
TARGET
RESPONSIBILITY
STATUS
KAIZEN SUSTENANCE
WHAT TO DO:- Drawing to be change
HOW TO DO:-
FREQUENCY :-
P15
After
ROOT CAUSE :- No size calculated for machining before Nitro carburizing
1
KAIZEN FINISH
Not Applicable
Machining stage Ø11.40 +0.010 | After nitro carburizing Ø11.45-0.03 | Growth
11.405-11.412 | 11.455-11.461 | 0.049-0.050
Before
Machining stage Ø11.4 -0.010 | After nitro carburizing Ø11.45-0.03 | Growth
11.394-11.398 | 11.420-11.428 | 0.023
Material send for HT. Lot is under monitoring.