## Slide 1
IDEA :- Gap between roller mounting edge & clamping block to be reduced by reversing the stopper plate
TPM CIRCLE NO :- 01
TPM CIRCLE NAME:
DEPT :- ASSEMBLY
CELL:- D comp
CELL NAME:- A325 Cam Assly.
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- Assembly
OPERATION :- Assly.
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A
C
D
S
M
KAIZEN THEME : To eliminate the C.C of the cam angle zero.
Problem present status :- Excess gap between roller mounting edge & clamping block.
COUNTERMEASURE:-
1) Gap between roller mounting edge & clamping block to be reduced (Before=5.95mm,After=4.10mm) by reversing the stopper plate & removing plate material by 0.7mm)
BENCHMARK
TARGET
KAIZEN START
TDC
398
0
10.08.2016
2.09.2016
TEAM MEMBERS : Mohan Kate, Nitin Sutar
,Supriya Patil
BENEFITS :-
No chances of generation of cam angle zero.
MANAGER’S SIGN: Janardan sathe
REGISTERED BY :- Mohan Kate
REGISTRATION NO. & DATE :- 10.08.16
WHY - WHY ANALYSIS :-
Why1 :- Cam angle found zero.
Why2 :- Roller getting tilt while roller clamping.
Why3 :- Excess gap between roller mounting edge & clamping block.
Why4 :- Weak Fixture design.
RESULT :-
SCOPE & PLAN FOR HORIZONTAL DEPLOYMENT
SR.
NO.
CELL
TARGET
RESPONSIBILITY
STATUS
KAIZEN SUSTENANCE
A394
WHAT TO DO:-.Point added in fixture validation sheet
HOW TO DO:- Gap checking by DVC.
FREQUENCY :- 3 months
P15
ROOT CAUSE : Weak fixture design.
1
Completed
KAIZEN FINISH
4.09.2016
23.09.16
After
Nitin Sutar
Before
Chart: Rejection in Nos.
| July | Aug | sep
rejection in PPM | 200 | 198 | 0