## Slide 1
IDEA : To have mechanism to reverse the tap
TPM CIRCLE NO :- 02
TPM CIRCLE NAME:
DEPT :-
CELL:-
CELL NAME:- Bracket SPM
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- A247 Bracket
OPERATION :- Tapping
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A
C
D
S
M
KAIZEN THEME : To eliminate tap breakages in power failure
Problem present status :- Frequent tap breakages in case of power failures. 198 numbers in April 16
COUNTERMEASURE:-
PLC logic modification to have in feed retraction of tap with anticlockwise rotation once the power has been resumed
BENCHMARK
TARGET
KAIZEN START
KAIZEN FINISH
198 / month
0
13.05.2016
30.05.2016
TEAM MEMBERS :
D Y Pawar
Sachin Chaudhary
BENEFITS :-
Production increased by 4242 no /
month
2) Tap cost saved
MANAGER’S SIGN :- SNC
REGISTERED BY :- Prakash & Sujit
REGISTRATION NO. & DATE :
WHY - WHY ANALYSIS :-
RESULT :-
KAIZEN SUSTENANCE
WHAT TO DO:-. Irreversible Kaizen.
HOW TO DO:-
FREQUENCY :-
P15
After
Before
ROOT CAUSE : No mechanism to reverse the tool
Why 1 – Tap breakages in power failure Why2 – Jerk on tap Why 3 – Tap gets trapped in the part as cycle interrupted at the time of power failures. Why 4 – No mechanism to reverse the tool when power resumes
Chart: Tap Breakages status
| 42461 | 42491 | 42522 | 42552
 | 198 | 173 | 0 | 0
After action implementation
Tap breakage phenomena eliminated
Availability of machine increased by
1400 min / month
Tap Trapped
Either break
Or thread damage