## Slide 1
IDEA :- Hob shifting frequency changed from 50 nos to 30 nos in hobing operation.
TPM CIRCLE NO :- 01
TPM CIRCLE NAME: Achiever
DEPT :- IQA
CELL:- A225
CELL NAME:- A225
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- Hobing
OPERATION :- Hobing
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A
C
D
S
M
KAIZEN THEME: To Eliminate rejection A225 shaft driving Burr stick on gear flanks
PROBLEM PRESENT STATUS :- A225 shaft driving Burr stick on gear flanks
COUNTERMEASURE:- 1.Hob shifting frequency changed from 50 nos to 30 nos in hobing operation.
2. 2)Gear Rolling checking operation started in finish stage to check high points and burr sticky detection.
BENCHMARK
KAIZEN START
87
TEAM MEMBERS : Dhananjay , Santosh,
Sachin, Sangita
BENEFITS :-
1) Avoid line mark rejection
MANAGER’S SIGN :-Sandip Patil, Sunil kinkar
REGISTERED BY :-IQA Team.
REGISTRATION NO. & DATE : 18.05.2016
WHY - WHY ANALYSIS :-
Why1 :- A225 shaft driving Burr stick on gear flanks
Why2 :-Excessive Hob Blunt.
Why3 :- Hob changing and shifting frequency is more.
RESULT :-
KAIZEN SUSTENANCE
WHAT TO DO:- Hob shifting
HOW TO DO:- Check visually.
FREQUENCY :-After 30 No’s
P15
ROOT CAUSE : Hob changing and shifting frequency is more.
SCOPE & PLAN FOR HORIZONTAL DEPLOYMENT |  |  | 
Sr. No | CELL | RESPONCIBILITY | STATUS
1 | A225 Geaer I | Mr. Khengat | Completed
KAIZEN FINISH
25.05.2016
TDC
18.05.2016
25.05.2016
TARGET
0
Before
After