## Slide 1
IDEA :- After grinding finish rotor drop in water bin.
KAIZEN NO :-
TPM CIRCLE NAME:
DEPT :- MACHINE SHOP
CELL:- Grinding
CELL NAME:- Rotor Grinding
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- Rimaco Grinding
OPERATION :- Surface grinding
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A,B,C
C
D
S
M
KAIZEN THEME : To Reduce Rejection for Dent Damage.
Problem / Present Status :-Rimaco -1 & 2 machine Rotor get damage due to rotor drop in bin then rotor metal to metal direct contact.
COUNTERMEASURE:- Out put rotor drop in water bin due to water avoid metal to metal direct contact and reduce gravitational force.
BENCHMARK
TARGET
KAIZEN START
TDC
Dent rej. Reduce
Zero dent rej.
02.05.2017
10.05.2017
TEAM MEMBERS : 1.Santosh Deshmukh
2. Sandip Jagtap
BENEFITS :-
1 .Dent damage rejection reduce.
MANAGER’S SIGN :- D. Y. Pawar
REGISTERED BY :- Santosh Deshmukh.
REGISTRATION NO. & DATE : 02.05.2017
WHY - WHY ANALYSIS :-
Why1 :-Finish output rotor drop in plastic bin.
Why2:- Rotor drop up to 300 mm distance
Why3 :-Rotor metal to metal direct contact.
Why4 :- Due to metal contact create dent.
RESULT :-
1) Rotor dent damage rejection reduce.
2) Operator rotor shorting time reduce incase of
rejection & rework during auto cycle.
3) Rotor 50 no’s lot after checking collect in finish bin.
4) Rotor cleaning activity done.
SCOPE & PLAN FOR HORIZONTAL DEPLOYMENT
SR.
NO.
CELL
TARGET
RESPONSIBILITY
STATUS
KAIZEN SUSTENANCE
WHAT TO DO:-
1. Used two big height bin with full water level.
2. Provide stand for bin.
HOW TO DO:-
1.Check every shift operator will be maintain minimum rotor output stock up to 50 no’s in bin.
2. Bin water level up 80 %.
P15
ROOT CAUSE :- Rotor metal to metal direct contact in output bin.
1
Done.
KAIZEN FINISH
08-05-2017
Rimaco -2
10-05-2017
SND
After
Before
AHPL/QMS/FR/09/E
Rev.No:01 Rev Date:15.12.2016