## Slide 1
IDEA :- Separate modified fixture to be provided for A314 oil pump assembly.
TPM CIRCLE NO :- 01
TPM CIRCLE NAME:
DEPT :- ASSEMBLY
CELL:- oil pump
CELL NAME:- A354
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- Assembly
OPERATION :- Plate fitment
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A
C
D
S
M
KAIZEN THEME : To avoid the mixing of A314 shaft into the A354 during assembly of pump.
Problem present status :- A314 shaft not detect in process during assembly of A354.
COUNTERMEASURE:-
Separate assembly fixture to be implement for A314 assembly so there is no need to adjust the length sensor during set up change
Fixture changing point is to be add in set up approval.
BENCHMARK
TARGET
KAIZEN START
TDC
30.09.2016
25.10.2016
TEAM MEMBERS : Amit Dhage, Nitin Sutar,
BENEFITS :-
1) To eliminate the customer complaint of wrong shaft mix-up
MANAGER’S SIGN :- Sandeep Patil
REGISTERED BY :- Amit Dhage
REGISTRATION NO. & DATE : 30.09.2016
WHY - WHY ANALYSIS :-
Why1 :- A314 shaft not detect in process during assembly of A354
Why2 :- Shaft total length Poke-Yoke disturb
Why3 :- Manual adjustment of shaft length sensor Why4:- Same assembly fixture for both products with common one sensor.
RESULT :-
SCOPE & PLAN FOR HORIZONTAL DEPLOYMENT
SR.
NO.
CELL
TARGET
RESPONSIBILITY
STATUS
KAIZEN SUSTENANCE
NA
WHAT TO DO:- Check point is to be added in set up approval .
HOW TO DO:- At the start of during set up change.
FREQUENCY :- During set up change.
P15
ROOT CAUSE : Same assembly fixture for both products with common one sensor.
1
NA
KAIZEN FINISH
NA
After
NA
Before